## Slide 1
SMART INDIA HACKATHON 2026
EchoEdge
Low Latency & Efficient Voice Activator for Edge Devices
Problem Statement ID
26172
Problem Statement Title
Low Latency and Efficient Voice Activator for Edge Devices
Theme
Smart Automation
PS Category
Hardware
Team ID
____________
Team Name
SEVA
Notes: Introduce team SEVA and the problem: voice-controlled edge devices that stream every second of audio to the cloud are slow, costly and privacy-invasive. EchoEdge fixes this with an always-on, tiny wake-word model at the edge that wakes the cloud ASR only after 'Hey Tara'.

## Slide 2
SEVA
EchoEdge: Proposed Solution
Smart India Hackathon 2026 | PS 26172 | Team SEVA
2
Proposed Solution
An open-source, microcontroller-class voice activator. A tiny on-device AI listens only for the custom wake word “Hey Tara” and, on detection, streams audio to a cloud ASR. The cloud hears nothing until the trigger, apart from a short pre-roll buffer.
Problem Addressed
Always-streaming mics are slow, costly and a privacy risk. EchoEdge gives instant voice activation on low-power hardware within the PS limits (<256 KB RAM, <10% idle CPU) using a 100% open-source stack with no commercial SDK.
How it works
Mic
I2S MEMS, 16 kHz
▶
Edge wake-word
DS-CNN, always on
▶
Pre-roll + VAD
1.5 s buffer, Silero
▶
Stream
Persistent WebSocket
▶
Cloud ASR
Moonshine transcript
EDGE DEVICE
NETWORK + CLOUD
Measured on our working prototype
37.7 KB
model size
9,649 parameters
0.64 ms
inference per 2 s
window (CPU)
~12x
fewer false accepts
120.6 to 10.3 per hour
~205-225 ms
keyword end to cloud
received (laptop)
100%
open-source
no commercial SDK
Prototype validated on a laptop as the edge stand-in; ESP32-S3 port and on-device benchmarking are the next milestone.
Notes: Walk the flow left to right. Edge side: mic, wake-word model, pre-roll and VAD. Cloud side: persistent WebSocket to Moonshine. Numbers are measured on the laptop prototype: 9,649-parameter model, 37.7 KB, 0.64 ms per window. False accepts fell from 120.6 to 10.3 per hour on 5.4 hours of unseen real speech after adding real-speech negatives. Latency of about 205-225 ms includes our deliberate two-consecutive-detection confirmation. State proactively that the ESP32 port is the next step.

## Slide 3
SEVA
Technical Approach
Smart India Hackathon 2026 | PS 26172 | Team SEVA
3
Technologies used
Hardware
ESP32-S3 + INMP441 I2S MEMS microphone
Edge model
Depthwise-separable CNN (DS-CNN) on 40-bin log-mel features; int8 via LiteRT for Microcontrollers
Training
PyTorch; 84 Piper-TTS voices + real recordings + LibriSpeech real-speech negatives
Voice activity
Silero VAD (ONNX, MIT) trims silence before streaming
Streaming
Raw PCM16 over a persistent WebSocket; Opus compression planned
Cloud ASR
Moonshine (MIT), real-time streaming, no GPU
Model: Conv stem, then 3 depthwise-separable blocks, global average pool, 1 logit
Methodology and process
1
Dataset and training
Synthetic voices + 7 real speakers; hard negatives, noise, reverb, SpecAugment
DONE
2
Edge-to-cloud pipeline
Wake word, pre-roll, VAD, WebSocket, Moonshine, live dashboard (laptop)
DONE
3
Quantize to int8
Export to LiteRT Micro; check accuracy drop
NEXT
4
ESP32-S3 firmware
I2S capture, on-device inference, Wi-Fi streaming
NEXT
5
On-device benchmark
RAM/flash, idle CPU %, false accepts, latency
NEXT
Notes: Explain the stack and why each piece was chosen: DS-CNN is the Hello Edge family designed for microcontrollers; Moonshine is MIT-licensed streaming ASR; Silero VAD removed hallucinated transcripts on silence. Phases 1 and 2 are complete and demonstrated live on a laptop. Phases 3 to 5 are the hardware milestones.

## Slide 4
SEVA
Feasibility and Viability
Smart India Hackathon 2026 | PS 26172 | Team SEVA
4
Technical Feasibility
Off-the-shelf parts: ESP32-S3 and INMP441 MEMS microphone.
9,649-parameter DS-CNN: 37.7 KB in float32, about 10 KB expected after int8, far below the 256 KB limit. Peak activation RAM will be measured on device.
DS-CNN is a proven keyword-spotting family (Hello Edge).
Execution Viability
Zero licensing cost: PyTorch, Piper, Moonshine (MIT), Silero VAD (MIT), websockets.
A full pipeline already runs live: mic, wake word, VAD, streaming, Moonshine, dashboard.
Parallel workstreams: data, firmware, ASR integration, testing.
Risk Mitigation
Unseen-speaker accuracy is ~71-75% with 7 speakers: we plan to record 15-20+ speakers, including more Indian accents.
False accepts: real-speech negatives cut them 120.6 to 10.3 per hour; TV and music soak tests are next.
Venue Wi-Fi or noise: local LED trigger indicator and a backup demo video.
False accepts per hour
Chart: 
| Before fix | After fix
False accepts/hour | 120.6 | 10.3
Soak test on 5.4 h of real, unseen audiobook speech through the exact live detection pipeline: about 12x fewer false triggers.
Notes: Be upfront about limitations: only 7 real speakers, so leave-one-speaker-out accuracy is about 71-75%; the fix is more speakers, not a new architecture. The false-accept soak test is the honest measure of real-world behaviour: 120.6 per hour before adding real-speech negatives, 10.3 after. We will also measure TV, music and more accents.

## Slide 5
SEVA
Impact and Benefits
Smart India Hackathon 2026 | PS 26172 | Team SEVA
5
TARGET AUDIENCE: ISRO and other edge/embedded users: satellites, ground stations, remote sensors, mission-control interfaces
BENEFITS
Economic
No licensing or SaaS fees; reuses low-cost ESP32 hardware.
Strategic / National
Indigenous, custom-trainable keywords; supports Atmanirbhar Bharat in critical space tech.
Environmental
Low idle draw suits solar and battery-powered remote nodes; no cloud polling.
Technical / Scalable
Keyword-agnostic pipeline: retrain for defence, disaster response or industrial IoT.
Social
Hands-free control for operators in noisy or hazardous field conditions.
IMPACT FOR ISRO
Data sovereignty and offline trigger.
Audio leaves the device only after the wake word (plus a short pre-roll), which suits launch pads and tracking stations with limited connectivity.
Hands-free operations.
Voice activation for ground-station operators and field engineers wearing gloves or suits.
Faster voice-triggered response.
Cloud is woken only on demand, for time-sensitive telemetry and command scenarios.
Notes: Tie each benefit back to ISRO. Emphasise data sovereignty: the cloud never hears audio before the wake word except a short pre-roll, and the open-source stack removes dependence on foreign proprietary voice SDKs.

## Slide 6
SEVA
Research and References
Smart India Hackathon 2026 | PS 26172 | Team SEVA
6
Solution | Open-source | Custom keyword | Fits PS constraints
Google / Alexa wake word | No | Fixed phrase | No (proprietary)
Porcupine (Picovoice) | No, proprietary | Yes, paid console | No (commercial SDK)
Espressif ESP-SR / WakeNet | Partly; training closed | Limited / paid service | Fails open-pipeline rule
Our approach: DS-CNN + LiteRT | Yes | Yes, self-trained | Targeted; verifying on ESP32
Key references
T. N. Sainath and C. Parada (2015), CNNs for Small-footprint Keyword Spotting, Interspeech.
Y. Zhang, N. Suda, L. Lai, V. Chandra (2017), Hello Edge: Keyword Spotting on Microcontrollers. arxiv.org/abs/1711.07128
P. Warden (2018), Speech Commands dataset. arxiv.org/abs/1804.03209
Moonshine: Speech Recognition for Live Transcription and Voice Commands. arxiv.org/abs/2410.15608
Silero VAD (MIT), github.com/snakers4/silero-vad
V. Panayotov et al. (2015), LibriSpeech: an ASR corpus based on public domain audio books, ICASSP.
LiteRT for Microcontrollers documentation. ai.google.dev/edge/litert/microcontrollers/overview
Opus Interactive Audio Codec, IETF RFC 6716. datatracker.ietf.org/doc/html/rfc6716
Espressif ESP-SR / WakeNet (industry comparison). github.com/espressif/esp-sr
Notes: The comparison shows why existing wake-word engines do not fit the PS: they are proprietary or have closed training. Our approach is open end to end. The last column is marked as targeted because on-device verification on ESP32 is our next milestone.